## Slide 1
HACKATHON · BUILD WITH AI: CODE FOR COMMUNITIES · TRACK 5
SurgeGrid AI
What the plan says, at the substation, at the right hour.
Chennai's power grid and flood console. Real rain, official maps, quoted plans.
surgegrid.web.app
Notes: One line: we built a tool a control room can trust because nothing on screen is invented.

## Slide 2
THE PROBLEM
The plans exist. Finding the right line in time is the hard part.
SurgeGrid AI · surgegrid.web.app
2 / 12
2.0 m
Chennai averages "barely 2.0 m above mean sea level". GCC City Disaster Management Plan
6 ft · 41
2015 floods: water up to 6 feet in substations, and 41 substations kept off. TANGEDCO Disaster Management Plan
Vardah
2016 cyclone: supply cut in many parts; fallen trees delayed restoration.
A control room has minutes, not hours, to find the right line for the right substation.
Notes: The pain is not missing plans. It is finding and applying them under pressure.

## Slide 3
OUR INSIGHT
The plans never give a number that forces a shut-off. So we don't invent one.
SurgeGrid AI · surgegrid.web.app
3 / 12
Official plans: supply may be switched off "if required". No wind speed or flood depth is given.
Many tools
Invent thresholds and present them as rules. A control room cannot tell which numbers are official.
SurgeGrid
We checked four plans and removed every rule they do not contain. The screen shows an operator decision, backed by the exact quote.
Notes: This is our differentiator: trust. A wrong invented trip level is worse than none.

## Slide 4
WHAT SURGEGRID DOES
Four things, in the order a control room needs them.
SurgeGrid AI · surgegrid.web.app
4 / 12
1 Replay
Cyclone Michaung in five steps: two before the peak, the peak, two after. Rain by area on the map.
2 Exposure
286 substations: yard elevation, official flood maps, and an exposed-now list at each step.
3 AI Directive
The official actions for this hour, each a quote with plan and page, and the substations they apply to.
4 Substation card
Flood facts, a copilot with quoted actions, GCC relief centres for the ward, and a backup suggestion.
Notes: Show the four things in that order during the demo.

## Slide 5
HOW IT WORKS
Real data in. Rules choose. Quotes speak. Gemini adds one note.
SurgeGrid AI · surgegrid.web.app
5 / 12
Real data
NASA IMERG rain ERA5-Land wind SRTM terrain OpenCity flood maps TNEB grid Live TANGEDCO notices
›
Rules
Phase from the data: watch, impact, restoration. Pick the substations.
›
37 quotes
Word for word, with plan and page, from four official plans.
›
Gemini 2.5
Words one short note. Cannot write or change a quote.
›
Screen
AI Directive and substation card.
Runs on Google Maps Platform · Earth Engine (scenario data) · Gemini via a Cloud Function · Firebase Hosting
Notes: Gemini is the last step and cannot change the quotes.

## Slide 6
REAL DATA
No synthetic storms. Everything replayed is real rain and wind.
SurgeGrid AI · surgegrid.web.app
6 / 12
Michaung, Dec 2023 (medians) | Satellite cell | IMD gauge
24 h to 08:30 IST, 3 Dec | 30 mm | 80 mm
24 h to 08:30 IST, 4 Dec | 147 mm | 190 mm
24 h to 08:30 IST, 5 Dec | 115 mm | 170 mm
286
substations, 2,678 feeders, 65,557 transformers, about 4.9 million consumers on mapped transformers
48 · 114
substations inside the 2015 flood extent · inside the 100-year flood-hazard map
162 · 120
GCC relief centres · wards they cover
Notes: We checked our satellite rain station by station against IMD's own gauges (17 gauges matched by exact name, coordinates from the Tamil Nadu gauge list; 7, 16 and 9 stations on 3, 4 and 5 Dec). The satellite cell held about a third of the gauge total on 3 Dec and two-thirds to three-quarters after, so the early steps look quieter than the gauges say. We show that and do not scale it up. Our wind (37 km/h) is also below IMD's Chennai stations (56 to 68 km/h, gusts 75 to 90). We deleted our earlier synthetic cyclone and two other events to focus on one real storm.

## Slide 7
THE AI
What Gemini does, and what it never does.
SurgeGrid AI · surgegrid.web.app
7 / 12
Does
Picks substation and feeder names from lists we send. Writes one short note, or a live-day summary of our data. Gemini 2.5 Flash on Google Cloud, no API key in the app.
Never does
Write, reword or cite the plan quotes. Invent a number: a note with a number not in the prompt is discarded.
GUARDRAILS
Fixed answer format
JSON schema
Names filtered
to our lists
Numbers checked
against the prompt
Gemini down?
Same quotes, rule-based notes
Notes: Meaningful AI work, with a safety design judges can inspect in gemini-proxy/ and geminiSopService.ts.

## Slide 8
LIVE DEMO · ABOUT 3 MINUTES
Watch one storm go from watch to restoration.
SurgeGrid AI · surgegrid.web.app
8 / 12
1
Open the site, pick Michaung. It starts at T-24h. The satellite rain is nearly clear (IMD's gauges read higher). The AI Directive shows 6 quoted actions with page numbers.
2
Press play: five steps, 6 seconds each. Rain fills in by cell, exposed substations get red rings, and IMD's own bulletin for each step is quoted under the timeline.
3
Point at a cell for its 24-hour rain and IMD class. Switch on the fixed official flood maps.
4
Open a low-lying substation: status line, Overview (flood facts), then Respond: copilot actions, relief centre, backup.
5
Open a substation inside no flood layer. It stays quiet: no false alarms.
Notes: End on the quote and page number: 'this is the plan's own text'.

## Slide 9
TRACK 5 FIT
What the brief asks, what we deliver, and the honest gaps.
SurgeGrid AI · surgegrid.web.app
9 / 12
The brief asks | We deliver | Honest gap
Earth Engine + real met data | IMERG rain, ERA5-Land wind, SRTM; Google Weather API | Wind is an area average
Simulate storm scenarios | One real hindcast (Michaung), five steps, rain by area | No storm surge or track; no flood prediction
Map grid and shelter exposure | 286 substations checked; 162 relief centres by ward | Centres have no coordinates
Early-warning advisories | Quoted actions per hour and substation; copy-SMS | No automatic dispatch
Gemini reasoning | Gemini 2.5 Flash notes with guardrails | Not multimodal
Notes: Judges reward honesty here; say the gaps out loud.

## Slide 10
BUILT FOR INDIA
Live today. National by design. Chennai only, for now.
SurgeGrid AI · surgegrid.web.app
10 / 12
Live today
surgegrid.web.app: static hosting plus one small Cloud Function. Keyless Gemini, origin allow-list, rate limit.
National by design
The MoP 2021 power-sector plan and IMD cyclone classes apply across India. City plans plug in as more quotes.
Repeatable
The scenario builder takes any area and date. City inputs sit in one config file.
The honest bit
Chennai only today. A new city needs its grid data, its local plan and its flood layers.
Notes: Do not claim more than this; present it as the roadmap.

## Slide 11
EVIDENCE AND HONESTY
We removed what we couldn't source, and say so.
SurgeGrid AI · surgegrid.web.app
11 / 12
Every plan line is a quote
Word for word, with plan and page. 37 quotes, each checked against the PDF text.
Removed: no plan says it
Wind and flood trip limits, restoration hours, a five-stage protocol, plinth heights, gang and pump counts.
Official maps, not model depths
Our flood score matched the city's 53 hotspots (AUC 0.76) but not the 2015 satellite map. So we show map checks.
Live site, Lighthouse
Accessibility 100. Desktop performance 91. Mobile performance 54, and we say so.
Notes: This is proof of engineering judgement, not a weakness.

## Slide 12
ROADMAP AND CLOSE
SurgeGrid AI puts the plan's own words in front of the operator, and makes no rule up.
Next
More storms and cities. Substations ranked by homes in mapped flood areas. Hospital and shelter exposure. Finer rain data. Tamil advisories. Faster mobile load.
Pilot path
A TANGEDCO or GCC control room uses it as a plan-lookup layer on its own grid data.
Live: surgegrid.web.app Repo: github.com/rsiva2294/surgegrid-ai
Notes: Finish with the live URL and the repo.